## Slide 1: Field bioinformatics
ARTIC TRAIN 03AUG22 Áine N O'Toole
ARTIC Network Train the Trainer - August 2022

## Slide 3
Nanopore bioinformatics
Goal:
…
> sample01
CTAGCATGCATCGTAGCTAGCTAGCTGATCGATGCTAGTCATGCTAGCTGATGCTAGTCGATGCTGATGCTAGTCGTGATGCTAGTCGATGCTAGTCGTAGCTAGTCGATGCTAGCTA
Squiggles
FASTA file

## Slide 4
Nanopore bioinformatics
Goal:
…
> sample01
CTAGCATGCATCGTAGCTAGCTAGCTGATCGATGCTAGTCATGCTAGCTGATGCTAGTCGATGCTGATGCTAGTCGTGATGCTAGTCGATGCTAGTCGTAGCTAGTCGATGCTAGCTA
>
Sequence name
Genome sequence
Squiggles
FASTA file

## Slide 5: First steps performed by MinKNOW

## Slide 6: 1. Basecalling
.fast5
ATGCATGC
.fastq

## Slide 7
guppy
1. Basecalling
@read
ATGCATGC
+
“$##€**’
.fast5
ATGCATGC
.fastq

## Slide 8: FASTQ

## Slide 9: FASTQ
header

## Slide 10: FASTQ
header

## Slide 11: FASTQ
header
@
unique read id
run id
read no.
channel
start time in pore

## Slide 12: FASTQ
nucleotide bases

## Slide 13: FASTQ
quality information

## Slide 14: FASTQ
header
nt bases
spacer
quality
Notes: So four lines

## Slide 15: Anatomy of a MinION read
Notes: To explain the next step we need to know a little bit about what are the different parts of information stored in each sequencing read. For nanopore data, if we work backwords in the wet lab protocol steps we can identify the parts of the read that exist in our data

## Slide 16
Tiled amplicon scheme
Notes: And remember we’re talking about tiled amplicon schemes here using the ligation kit for nanopore. This is specific to the artic scheme and won’t necessarily directly correspond to other seq techs or protocols

## Slide 17
Tiled amplicon scheme
Notes: The amplicons themselves are only a part of the reads.

## Slide 18: Adaptors
Notes: Adaptors are the last things that get added before the sequencing run so they’re on the ends

## Slide 19: Adaptors
Notes: Little bits of DNA with a protein ligated to it

## Slide 20: Barcodes
Notes: Again working backwords through the wet-lab protocol, barcodes were added

## Slide 21: Barcodes
Sample 1
Sample 2
Sample 3
Notes: Barcodes are little unique nucleotide sequences that get stuck on to each sample- so the barcode sequence allows you to id which sample each read is from

## Slide 22
Notes: And because everything gets pooled together for nanopore data, we’ve got all our samples in one tube, the reads that get produced are a mixture

## Slide 23
2. Demultiplexing
Notes: And identifying what barcodes are part of what sample is called demultiplexing

## Slide 24
guppy
2. Demultiplexing
barcode01
barcode02
Unassigned

## Slide 25
barcode01
barcode02
Unassigned
basecalling
demultiplexing
Notes: In summary, the data you get out of minknow will be basecalled and demultiplexed. But we still have a long way to go to get to the final fasta sequence file

## Slide 26
ARTIC Network Field Bioinformatics

## Slide 27
ARTIC Network Field Bioinformatics
Notes: Created by nick loman in 2016 and then was updated extensively in 2020 at the start of the sarscov-2 pandemic by will rowe

## Slide 28
…
> sample01
CTAGCATGCATCGTAGCTAGCTAGCTGATCGATGCTAGTCATGCTAGCTGATGCTAGTCGATGCTGATGCTAGTCGTGATGCTAGTCGATGCTAGTCGTAGCTAGTCGATGCTAGCTA
FASTA file
ARTIC Network Field Bioinformatics

## Slide 29
ARTIC Network Field Bioinformatics
Best practice bioinformatic pipeline

## Slide 30
ARTIC Network Field Bioinformatics
Best practice bioinformatic pipeline
For tiled amplicon schemes

## Slide 31
ARTIC Network Field Bioinformatics
Best practice bioinformatic pipeline
For tiled amplicon schemes
Command line tool or …

## Slide 32
ARTIC Network Field Bioinformatics
Notes: It has also been implemented in epi2me which is an interface for running pipelines that nanopore provide.

## Slide 33
ARTIC Network Field Bioinformatics
barcode01
Notes: So because of minknow we have directories on the computer with lots of reads for each barcode.

## Slide 34
ARTIC Network Field Bioinformatics
barcode01
Notes: The reads still have stuff of on the end that we don’t want contributing to our end sequence.

## Slide 35
ARTIC Network Field Bioinformatics
barcode01
?
Notes: We also want to make sure that the actual stuff in the sequence is what we think it is, so figure out if it’s sars-cov-2, and also figure out what part of the genome it corresponds to

## Slide 36
ARTIC Network Field Bioinformatics
align_trim
Notes: So this is what one of the first stages of the pipeline does- called align trim

## Slide 37: Align to reference
Reference genome
Pool 1
Pool 2
Notes: In order to find out what parts of the reads correspond to what parts of the genome we align against the reference- ref on top, example of the amplicons we’re expecting to see based on our lab protocol. Remember there are two pools of primers.

## Slide 38: Align to reference
Reference genome

## Slide 39
Notes: If we revisit the anatomy of a read

## Slide 40: Adaptors
Notes: Adaptors are the last things that get added before the sequencing run so they’re on the ends

## Slide 41: Barcodes
Notes: Again working backwords through the wet-lab protocol, barcodes were added

## Slide 42: Primers
Notes: The next thing is the primer sequences- which will be identical to the reference, so we don’t want to include these in our final output either

## Slide 43: Sequence of interest
Notes: So it’s really the middle bit highlighted here is what we’re interested in getting out at the end

## Slide 44: Align to reference
Reference genome

## Slide 45
If it does not align:
Low quality read
Contamination (human?)
Reference genome

## Slide 46
If it does not align:
Low quality read
Contamination (human?)
Throw them away
Reference genome

## Slide 47
Amplicon 2
Read Group 2
Reference genome

## Slide 48
Reads assigned an
-amplicon
-read group
based on where they align
Reference genome

## Slide 49
This alignment process produces a map of where along the genome the reads belong
SAM (sequence alignment map)
Reference genome

## Slide 50
Amplicon
Coverage
Overlap = double coverage

## Slide 51
@HD VN:1.3 SO:coordinate
@SQ SN:ref LN:45
@SQ SN:ref2 LN:40
r001 163 ref 7 30 8M4I4M1D3M = 37 39 TTAGATAAAGAGGATACTG * XX:B:S,12561,2,20,112
r002 0 ref 9 30 1S2I6M1P1I1P1I4M2I * 0 0 AAAAGATAAGGGATAAA *
r003 0 ref 9 30 5H6M * 0 0 AGCTAA *
r004 0 ref 16 30 6M14N1I5M * 0 0 ATAGCTCTCAGC *
r003 16 ref 29 30 6H5M * 0 0 TAGGC *
r001 83 ref 37 30 9M = 7 -39 CAGCGCCAT *
SAM (sequence alignment map)

## Slide 52
@HD VN:1.3 SO:coordinate
@SQ SN:ref LN:45
@SQ SN:ref2 LN:40
r001 163 ref 7 30 8M4I4M1D3M = 37 39 TTAGATAAAGAGGATACTG * XX:B:S,12561,2,20,112
r002 0 ref 9 30 1S2I6M1P1I1P1I4M2I * 0 0 AAAAGATAAGGGATAAA *
r003 0 ref 9 30 5H6M * 0 0 AGCTAA *
r004 0 ref 16 30 6M14N1I5M * 0 0 ATAGCTCTCAGC *
r003 16 ref 29 30 6H5M * 0 0 TAGGC *
r001 83 ref 37 30 9M = 7 -39 CAGCGCCAT *
Header information
Alignment information
SAM (sequence alignment map)

## Slide 53
Reference genome
Mask out the part of the read we don’t want
Softmasking

## Slide 54
trimmed
primer trimmed
Reference genome

## Slide 55
Amplicon
Overlap = double coverage
Coverage

## Slide 56: Normalise coverage across genome
Coverage

## Slide 57: Sequence of interest
Notes: But it’s not quite as straightforward as that, we have the part of the read we care about,

## Slide 58: Sequence of interest (with error)
Notes: But Because of the error rate of nanopore, each read will have a proportion of unique errors

## Slide 59: Sequence of interest (with error)
SNPs
Deletions
Insertions
Notes: These can be point mutations or snps, deletions and insertions.

## Slide 60
Nanopore error is biased towards
Homopolymers
Low complexity regions
Notes: These can be point mutations or snps, deletions and insertions.

## Slide 61
Nanopore error is biased towards
Homopolymers
Low complexity regions
Notes: These can be point mutations or snps, deletions and insertions.

## Slide 63
nanoporetech.com
95-97% 1D single molecule accuracy

## Slide 64: Sequence of interest (with error)
Notes: So it is getting better, but

## Slide 65
Notes: But they’ll be different between different reads

## Slide 66: Sufficient depth & coverage
Notes: But they’ll be different between different reads

## Slide 67: Call variants
Variant called

## Slide 68
Reference genome

## Slide 69
Reference genome
Read Group 1
Read Group 2

## Slide 70: Call variants Read Group 1
Reference genome

## Slide 71: Call variants Read Group 2
Reference genome

## Slide 72
Reference genome
Merge variants from the two read groups together

## Slide 73
Quality check all variants called
Coverage

## Slide 74
Quality check all variants called
Coverage too low
Coverage

## Slide 75
Quality check all variants called
Coverage too low
Depth mask
Coverage

## Slide 76
Reference genome
Call consensus sequence (bcftools)

## Slide 77: Recap
Basecalling
Demultiplexing
Align vs reference
Mask unwanted part of reads
Normalise depth
Call variants (RG1 and RG2)
Merge variants
QC filter variants
Mask low depth of coverage
Call consensus